REST on your SoC with Device::WebIO

---
Wanted to Open my Garage

---
Based on WebIOPi
- REST API or Python interface
- Specific to Raspberry Pi
- “GPIO expanders” (stuff directly hooked to Rpi)
- Implements many sensors (temp, humidity, gyro, etc.)

---
Wanted something that could support many boards (Rpi, Banana Pi, PCDuino, Edison, Firmata/Arduino, etc.), and a video interface

---
Perl API
my $webio = Device::WebIO->new;
my $rpi = Device::WebIO::RaspberryPi->new;
my $firmata = Device::WebIO::Firmata->new({
port => '/dev/ttyACM0',
});
$webio->register( 'rpi', $rpi );
$webio->register( 'firmata', $firmata );
$webio->set_as_input( 'rpi', 17 );
$webio->set_as_output( 'firmata', 13 );
my $input = $webio->digital_input( 'rpi', 17 );
$webio->digital_output( 'firmata', 13 );

---
[Demo]

---
REST API
Val = GET http://localhost:8080/devices/rpi/17/value
POST http://localhost:8080/devices/firmata/13/value/Val

---
Device::WebIO::Dancer
- Implements the REST API
- Deploy like any other Dancer (Plack) app

---
Raspberry Pi (Model B+) – $40
- 700 MHz Broadcom BCM2835 (ARM)
- 512MB RAM
- 4 USB
- HDMI
- Ethernet
- Camera connector
- No on-board WiFi, Bluetooth
- Runs off micro SD card

---
Arduino Uno (Firmata) – $25
- Atmega328 @16MHz
- “Harvard” architecture
- 32KB flash (program storage)
- 2KB RAM (data storage)
- WiFi/Ethernet shileds available
- Firmata can take instructions from Perl over USB

---
PCDuino2 – $65
- 1GHz A8
- 1GB RAM
- 4GB onboard flash
- HDMI
- 1 USB
- Arduino pin compatible
- On-board WiFi, ethernet

---
Banana Pi – $60(ish)
- 1GHz A7 Dual Core
- 1GB RAM
- I/O similar to Raspberry Pi Model B
- SATA port

---
Intel Edison – $50
- 500MHz Intel Atom
- 1GB RAM
- WiFi, Bluetooth
- Seperate cable exposes 40 GPIO pins
- Size of an SD card

---
Cubieboard2 – $65
- A7 Dual Core
- 1GB RAM
- HDMI
- Ethernet
- SATA
- Tons of I/O pins
- Runs off micro SD card

---
MiniSpartan6+ – $60(ish)
- Kickstarter
- LX9 FPGA
- 32MB RAM
- 2xHDMI (input or output)
- MicroSD card

---
Please use good power adaptors
(>750mA, at least)

---
How can we run all of these with the
same library?

---
Abstraction with Moo Roles
- Devices have different capabilities, specified by roles
- PCDuino can do Analog-to-Digital conversion, so it has ADC role
- RaspberryPi doesn't, so it doesn't
- Roles for:
  - GPIO
  - ADC
  - I2CProvider
  - PWM
  - StillImage/Video

---
I2C Devices
- I2CProvider – Something that can read/write i2c devices directly
- I2CUser – Implements some specific I2C device
- Implement once, run anywhere
  - (That's the idea, anyway)

---
Sensors
- Currently: TMP102 temperature sensor
- Future:
  - Barometric pressure
  - Luminosity
  - Distance
  - Accelerometers
  - Gyros
  - GPS

---
Implementing a Sensor
- I2C bus
  - Two lines: SDA (data) and SCL (clock)
    - (Plus power and ground)
- Each I2C device has an address
  - Allows multiple devices on same bus
  - Raspberry Pi, find using “i2cdetect”
    - It's probably safe
- “Register” can hold or be given values for functions
- Find much of this info on the datasheet

---
Let's all have fun while
reading datasheets!
Obnoxious Slide

---
We now return you to dreary slides

---
Implementing TMP102
- Do the 'Device::WebIO::Device::TempSensor' role
- 'temp_celsius()' reads from device
- 'temp_kelvin()' and 'temp_fahrenheit()' convert from celsius
- [See TempSensor code]
- [Demo]

---
REST Interface
- Adapted almost-verbatim from WebIOPi
- Corrected a few
- Added a few others
- Full documentation in Device::WebIO::Dancer dist, in pod/rest_api.pod

---
REST Interface
- Most have the form: /devices/[name]/[function]/[channel]
- [name]: Name of device registered in $webio
- [function]: Kind of thing you're doing (analog, pwm, etc.)
- [channel]: A specific thing to connect to, often a pin
- Be sure to use GET/POST correctly
  - You'll get an unexpected 404 if you confuse them

---
REST: Deploy to Apache
It's Dancer, so Plack, so deploy like anything else under Plack/Dancer

---
Raspberry Pi PSGI
use Device::WebIO::Dancer;
use Device::WebIO;
use Device::WebIO::RaspberryPi;
use Plack::Builder;
my $webio = Device::WebIO->new;
my $rpi = Device::WebIO::RaspberryPi->new;
$webio->register( 'rpi', $rpi );
Device::WebIO::Dancer::init( $webio, 'rpi' );
builder {
        dance;
};

---
Apache Config
<Location />
        SetHandler perl-script
        PerlResponseHandler Plack::Handler::Apache2
        PerlSetVar psgi_app /path/to/raspberrypi.psgi
        AuthType Basic
        AuthName "Restricted"
        AuthBasicProvider file
        AuthUserFile /path/to/passwd/file
        Require valid-user
</Location>
<Location /app>
        SetHandler none
</Location>

---
[Demo GPIO App]

---
Security? What Security?
- Most secure: don't have REST interface
- Next best: only respond on localhost
- Next best: only respond to internal network
- Next best: SSL, client certs, or 20-char password made of 90 possible character codes

---
Questions?